## Slide 1: Do the Numbers Hold on Real Hardware?
A reproducibility and measurement audit of a low-cost hybrid ECC authentication protocol for IoT
Jay Kerkar · Chaitanya Kelkar · Chirag Poornamath · Yash Kolekar
Project guide: Dr. Shanta Sondur
Notes: We audited a 2026 IEEE TCE paper on lightweight IoT authentication: we implemented its protocol, ran it on a real microcontroller, and re-checked its cost claims with measured numbers.

## Slide 2: Tiny devices need cheap authentication
The device is weak
Little memory and a slow processor, so heavy cryptography is costly.
It must prove who it is
Device and server authenticate each other before any data is exchanged.
The base paper claims savings
Al-Rasheed et al., IEEE TCE 72(2), May 2026, proposes a lighter protocol.
Claimed reduction vs. prior schemes
17%
communication
21%
processing
12%
storage
Notes: The base paper says its protocol is about 17% cheaper in communication, 21% in processing and 12% in storage than earlier schemes. Our question: do those numbers hold on real hardware?

## Slide 3: The protocol: two messages, one shared key
IoT device
holds secret λ
Server
holds secret λ
M1 fresh pseudonym, encrypted nonce Ni, tag
M2 server nonce Nj, proof it knew the secret
Both sides then compute the same session key
K = KDF( k* ‖ Ni ‖ Nj ‖ t )
Where is the ECC?
Only offline, when a trusted authority issues secrets. Online: hashes, AES-GCM, HKDF.
Notes: The paper's Section III protocol. The device sends a one-time pseudonym with an encrypted nonce; the server answers with its nonce and a proof; both derive the session key. The elliptic-curve part is only used during offline registration, hence 'hybrid'.

## Slide 4: How the paper argued it is cheap
cost = n_hash × T_H + n_enc × T_SE/D + n_ECC × T_ECM
T_H (assumed)
0.32 ms
one SHA-1 hash
T_SE/D (assumed)
5.6 ms
one symmetric encrypt / decrypt
T_ECM (assumed)
17.1 ms
one ECC scalar multiplication
These prices were assumed, not measured. The OMNeT++ simulation behind Fig. 1 has no published code, scenario or data, so it cannot be re-run.
Notes: The paper counts operations and multiplies by assumed per-operation times, plus an OMNeT++ simulation that nobody can re-run. That is why there is no 'dataset': a protocol-cost paper's reproducible inputs are the specification, the constants and the operation counts, and we used all three.

## Slide 5: What we did
1 Audit
Checked every table and figure against the paper's own text.
2 Implement
Python reference plus an independent C core, equation by equation.
3 Measure
ESP8266 at 80 and 160 MHz, cloud Graviton2, laptop. Median of 100 runs.
4 Recompute
Re-ran the paper's own cost model with measured prices.
108 tests pass. The C device on the ESP8266 and the Python server complete 20 of 20 handshakes with identical session keys; replays are rejected.
Notes: We implement Section III of the base paper (the nonce-based protocol), not the replayable Section II variant. Same C source on every platform so the comparison is fair.

## Slide 6: Finding 1: numbers don't reproduce
0 of 9
ways of computing 17 / 21 / 12 % from the paper's own tables give those values.
What is reported | Table IV | Text
Messages | 4 | 2
Bits | 1,024 | 264
Fig. 1 is captioned “processing”, but its axis shows communication overhead.
One competitor row has its device and server counts swapped.
The simulation cannot be re-run, so Fig. 1 cannot be checked.
Notes: We do not say the authors' simulation is wrong. We say the headline percentages cannot be derived from what was published, and the paper's table contradicts its own text.

## Slide 7: Finding 2: the assumed prices are wrong
Chart: ECC op cost, in SHA-1 hashes
| Paper's assumption | Measured on ESP8266
ECC cost in hash units | 53 | 7604
Operation | Assumed | Measured | Off by
ECC P-256 | 17.1 ms | 276 ms | 16× slower
SHA-1 | 0.32 ms | 0.036 ms | 8.8× faster
AES-GCM | 5.6 ms | 0.5–1.2 ms | 5–12× faster
Same C source on every platform; ratios are identical at 80 and 160 MHz and on a second board. Medians of 100 runs.
ECC is far costlier, and symmetric crypto far cheaper, than the paper's cost model assumes.
Notes: On the ESP8266 a P-256 scalar multiplication takes 276 ms, 16 times the paper's constant, while hashing and AES-GCM are 5 to 12 times cheaper than assumed. The ratio of ECC to hash is 7,604 against an assumed 53.

## Slide 8: Finding 3: the ranking cuts both ways
Versus ECC-based schemes
60–2,520×
cheaper than the paper claims. The scheme wins, by far more than reported.
Versus hash-only schemes
3.8–13.7×
more expensive, once the session-key derivation is counted. The paper says the opposite.
Why: the paper's own Eq. 16 needs a key-derivation step (HKDF, 629 µs, about 17 hashes) that its cost table leaves out.
Notes: The ranking flips back only if the symmetric step is read as unauthenticated AES, which would drop the MAC the protocol requires. We report four readings of the cost and say which one we think is right.

## Slide 9: Finding 4: no forward secrecy
1 Record
An attacker saves encrypted sessions today.
2 Steal
Later, the long-term secret k* leaks.
3 Decrypt
Every past session key is rebuilt: 5 of 5 in our test.
Why: K = KDF(k* ‖ Ni ‖ Nj ‖ t) uses no ephemeral secret, so k* plus recorded traffic rebuilds K. Fixing it needs a fresh key exchange per session, which is an ECC operation (276 ms on our chip).
Notes: This is an attack script, not a formal proof. It shows the design property: compromise of the long-term secret exposes all past sessions.

## Slide 10: Finding 5: the server does a hidden loop
for device in all_devices:
for t in epoch_window:
if H2(device.secret, t) == pid:
return device
Pseudonyms change every message, so the server cannot look one up. It tries every device, and the cost grows with the fleet. The paper's table treats server cost as a constant.
Chart: Server lookup per request (ms)
| 1,000 devices | 5,000 devices
Lookup time (ms) | 4.8 | 23.9
A precomputed table removes the loop at the price of memory (about 416 KB in our setup).
Notes: Measured with a 13-epoch window. This is a scaling cost the paper's operation-count table cannot show.

## Slide 11: It does run on a real microcontroller
5.26 ms
device compute per handshake
1.67 build + 3.59 verify
216 B
first message (M1)
52 ms over Wi-Fi
276 ms
one ECC multiplication
on the same chip
≈ 52×
that ECC op vs. the whole handshake
276 ms ÷ 5.26 ms
The protocol itself is genuinely light. The paper's weakness is its evidence and its constants, not the idea.
Notes: This is an ESP8266 at 80 MHz. We are fair to the protocol: it is cheap online. Our critique is about the evidence behind the headline percentages.

## Slide 12: What we show, and what we don't claim
We show
Headline savings are not derivable from the published tables
Cost constants are off by 16× and 5–12×
The ranking depends on counting the KDF
No forward secrecy; server cost grows with devices
We do not claim
That the authors' simulation is wrong, only that it cannot be reproduced
Results beyond one ESP8266 and one crypto library
That we re-implemented the rivals; two table rows were matched via secondary sources only
A formal security proof; the authors were not contacted
Notes: Be upfront about the limits: single MCU, single library, competitors not re-implemented, no formal analysis, authors not contacted.

## Slide 13: Take-away
The savings cannot be reproduced from what was published. On real hardware the scheme beats ECC-heavy rivals by a wide margin, loses to hash-only ones, has no forward secrecy, and its server cost grows with the fleet.
Base paper: Al-Rasheed et al., IEEE Trans. Consumer Electronics 72(2), 4483–4491, May 2026. DOI 10.1109/TCE.2026.3662053
Notes: One sentence: the numbers do not hold as published; the protocol is still cheap, but not in the way, or by the margin, the paper says.